Zoom on source region
Source: 5 cells
[Speaker Notes: Source region is from 0 to 0.8 m, over 5 cells Multiplier of ion sound speed = 10]

---
Slow electrons never get out here!
They sort themselves by speed
[Speaker Notes: I set the ion-drift-multiplier to zero. This caused the particle weights to become zero and so no electric field is generated!]

---
[Speaker Notes: Te = 0.01 eV. The ‘spray’ is the over-accelerated electrons]

---
run1
N=300
Ion accumulation near r=0 accelerates electrons
[Speaker Notes: Cut timestep by 10]

---
N=500

---
N=600
Numerical acceleration near r=0
On-axis spike has appeared; leads to above

---
run1
N=1000
Numerical acceleration of electrons dominates
[Speaker Notes: Reduced timestep by 10. Ran to 1000 steps.]

---
sphere1D/runs/14oct18
1000 steps; dt=1e-6 s
Density climbs in center. May be reaching equilibrium, or may need some heating.
Need a diagnostic to check the temperature & flux.
[Speaker Notes: Plot used sphere1D-ne-ni.pvsm Input summary: 2 cell/Debye length. 25 Debye lengths in region. Uniform mesh. timestep=1e-6 s is slightly over vstream=0.3. Ion mass is 100 electrons. 3 electrons per cell; 1 ion per cell. Potential is flat at r=0. Applied random E-field is zero.]

---
[Speaker Notes: Profile with most terminal output turned off.]

---
[Speaker Notes: Times for previous page plot.]

---
Using C++ functions, the particle density calculations are almost negligible!

---
Using C++ functions, the particle density calculations are almost negligible!